## Slide 1
TEAM 1 · REPO
TE3002B · Mobile Robotics
MINI CHALLENGE 5
Line Following
& Traffic Light Control
Closed-loop PID navigation using computer vision · PuzzleBot

## Slide 2
The Challenge
Part 1 — Line Following
Follow a black line on a physical track using the robot camera — no GPS, no pre-defined waypoints.
The camera becomes the sensor. The line centroid is the setpoint. A PID controller drives angular velocity to keep the robot centered on the track.
Track: 3 parallel black lines on a tan mat, with curves and an intersection.
Part 2 — Traffic Light
Integrate real-time color detection with the line follower:
Red — full stop (latched until green)
Yellow — slow down to 40% speed
Green — resume normal speed
The robot must not move again until it sees several consecutive green frames — not just one.

## Slide 3
System Architecture
Camera
(ros_deep_learning)
line_detector.py
traffic_light
_detector.py
controller.py
(line_following mode)
cmd_vel_bridge.py
Hackerboard
(ESP32 firmware)
odometry_node.py
/video_source/raw
/line_error
/line_detected
/semaphore_state
/cmd_vel
L/R Velocity
/robot_pose

## Slide 4
Line Detection — Vision Pipeline
1
Camera
Frame
640×480 BGR
2
Crop ROI
Bottom 30%
of image
3
Grayscale
+ Blur
Gaussian 5x5
4
Adaptive
Threshold
BINARY_INV
local contrast
5
Morphology
Open + Close
Noise removal
gap filling
6
Connected
Components
Label blobs
filter area + AR
7
Centroid
Average
Error = (cx - W/2)
/ (W/2)
Why Connected Components + Moments?
Each black line becomes a labeled blob. Area and aspect-ratio filters reject floor noise and crosswalk dashes automatically (dashes are wide + short; track lines are tall + narrow in the ROI). Averaging the 3 centroids gives a stable center error signal that is robust to partially visible lines.
Control Error = ( cx_avg − W / 2 ) / ( W / 2 ) ∈ [ −1 , +1 ]
−1 = line far left | 0 = centered | +1 = line far right

## Slide 5
Controller & Traffic Light Integration
PID Line Controller
ω = Kp · error + Ki · ∫error + Kd · Δerror
v = v_base · ( 1 − factor · | error | )
Angular velocity (ω) is driven by a PID on the pixel error.
Linear velocity (v) automatically reduces in curves when the error is large — no extra curve-detection logic needed.
Line lost? Hold last ω for 0.4 s, then full stop. Prevents blind driving off the track.
Traffic Light Debounce
RED
Full stop. Latch stays ON until green confirmed.
YELLOW
Speed scaled to 40%. Angular correction continues.
GREEN
Normal operation. 5 consecutive frames to unlatch.
Key: Requires N consecutive frames before confirming a color. Debug image shows a live progress bar.

## Slide 6
Tuning & Robustness
Vision Parameters
roi_top_ratio
0.55
Where in the frame to look for the line
threshold_c
8
Most impactful single value — tune first
min_blob_area
300 px
Rejects small noise blobs
min_aspect_ratio
0.8
Rejects flat crosswalk dashes
debounce_frames
5
Frames before color state is confirmed
Controller Parameters
kp_line
0.5
Main steering gain — tune first
kd_line
0.05
Damps oscillation on straights
v_line_base
0.10 m/s
Base forward speed
speed_curve_factor
0.5
Slowdown in curves: v*(1-f*|e|)
line_lost_timeout
0.4 s
Grace period at intersections

## Slide 7
Results & Conclusions
✓ Line Following
Robot follows 3-line track through curves and straights. Speed automatically reduces in turns proportional to error.
✓ Intersection Handling
Aspect-ratio blob filter rejects crosswalk dashes. Line-lost grace period lets the robot coast through the gap.
✓ Traffic Light
5-frame debounce eliminates false positives. Asymmetric latch: one red frame stops; multiple greens needed to go.
✓ Backwards-Compatible
All previous MC2-MC4 modes (sequential, simultaneous, waypoints) still work — only additive changes were made.
Team 1 · REPO — TE3002B Mobile Robotics — Tecnológico de Monterrey